## Slide 1: Wireless OBD-2 Diagnostic Tool with touchscreen
Zak Rowland
Senior Project Proposal

## Slide 2: My Solution
Small Bluetooth transceiver powered by the OBD-2 port to send data
Handheld unit will include:
  Single board computer (such as Raspberry Pi Zero W)
  A Bluetooth transceiver
  Resistive touchscreen
  Rechargeable battery via Micro USB
  Simple user interface
  Basic functionality to keep costs low

## Slide 3: System Block Diagram

## Slide 4: What will that look like?
Micro USB
Touchscreen
Power Button
Magnet

## Slide 5: What about the ui?
Trouble Codes
Battery Status
Scroll Up and Down
Sensor Data
Settings

## Slide 6: What about the current tools that exist?
One product is the low-cost Bluetooth readers that connect to a phone app
source
How is my solution better?
  No sketchy software to install on your phone
  Dedicated handheld unit
    Can be mounted with magnet
    Phone can be used for other things
  Single board computer is reprogrammable
    Features can be added if the user desires
    Open source

## Slide 7: What about the current tools that exist?
Another product is this Wi-Fi connected unit that is similar to my proposed solution
source
How is my solution better?
  The unit pictured is over $500
    My target is under $150
  Simple, more user-friendly interface
    Only includes most necessary features
  Single board computer is reprogrammable
    Features can be added if the user desires
    Open source

## Slide 8: Requirement Examples
The system shall work with the 2008 Nissan Altima OBD-II protocol
  ISO15765-4 (CAN-BUS)
  Other vehicles may work however it is not a requirement
The Bluetooth transceiver circuit that interfaces with the OBD-II port shall be powered by the OBD-II port
  A power circuit will be designed to ensure power from the port is reliable

## Slide 9: Another Requirement Example
The handheld unit shall use a resistive touchscreen to display information and receive user input
  The touchscreen of the handheld unit shall be 3.5” or greater diagonally
  The touchscreen of the handheld unit shall operate at a resolution of at least 320 x 480 pixels
  Resistive instead of capacitive because
    Cost is lower
    Can be used with gloves (or anything really)
    Swiping or gestures won’t be used

## Slide 10: Why is this product worth developing?
There is no wireless low-cost unit with the basic features that I described that doesn’t connect to a smart phone
Open source code and documentation allows the product to be improved or features be added as the end user sees fit
I will learn about many new protocols and hardware including OBD-II, CAN, Bluetooth, touchscreen interfacing, and more